## Slide 1: Introduction to Cortex-M4 Programming

## Slide 2: Module Syllabus
Program Code
  C Language vs. Assembly Language
  Program-Generation Flow
  Cortex-M4 Program Image
Program Data
  How is Data Stored in RAM
  Data Types
  Accessing Data using C and Assembly
Mixed Assembly and C Programming
  Calling a C Function from Assembly
  Calling an Assembly Function from C
  Embedded Assembly

## Slide 3: Program Code

## Slide 4: Program Code Overview
All microcontrollers need a program code to perform an intended task
The program of embedded systems is usually developed at a relatively lower level
  Less support from operating systems
  Lack of standard programing interface
  Often hardware specific, e.g. memory usage constraints, available instructions etc.
Programming language
  Embedded systems are usually programed using C (or C++) language and assembly language
  ARM-based tools can compile the C code or the assembly code to the executable file, which can be executed by ARM-based processors
  A completely integrated program code can be also referred as a program image or an executable file

## Slide 5: C Language vs. Assembly Language
Language | Advantages | Disadvantage
C | Easy to learn | Limited or no direct access to core registers and stack
 | Portable | No direct control over instruction sequence generation
 | Easy handling of complex data structures | No direct control over stack usage
Assembly | Allow direct control to each instruction step and all memory | Take longer time to learn
 | Allows direct access to instructions that cannot be generated with C | Difficult to manage data structure
 |  | Less portable

## Slide 6: Typical Program-Generation Flow
The generation of program follows a typical development flow
  Compile  Assemble  Link  Download
  The generated executable file (or program image) is stored in the program memory (normally an on-chip flash memory), to be fetched by the processor
Data Output
C Code
Assembly Code
Object Code
Libraries
Program Image
Compile
Assemble
Link
Download
Program Memory
Fetch
Decode
Execute
Processor
Processing
Data Input
Instruction
Fetch
Off-line Compilation
Typical program-generation flow

## Slide 7: Compilation using ARM-based Tools
C/ C++
armcc
armasm
C/ C++
C/ C++
C/ C++
C/ C++
Assembly
C/ C++
C/ C++
Object
C/ C++
C/ C++
Libraries
armlink &
armmar
Image
binary
.O Files
.S Files
.AXF File
.LIB file
.BIN File
.HEX File
Disassembly File
C, C++
ASM files
Compile/ assemble
Link
executable

## Slide 8: Compiler Stages
Parser
  Reads in C code,
  Checks for syntax errors,
  Forms intermediate code (tree representation)
High-Level Optimizer
  Modifies intermediate code (processor-independent)
Code Generator
  Creates assembly code step-by-step from each node of the intermediate code
  Allocates variable uses to registers
Low-Level Optimizer
  Modifies assembly code (parts are processor-specific)
Assembler
  Creates object code (machine code)
Linker/Loader
  Creates executable image from object file

## Slide 9: Cortex-M4 Program Image
What is a program image
  The program image (or sometimes referred as executable file) usually refers to a piece of fully integrated code that is ready to execute
In Cortex-M4, the program image includes:
  Vector table – includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP)
  C start-up routine
  Program code – application code and data
  C library code – program codes for C library functions

## Slide 10: Cortex-M4 Program Image
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
Image
0x00000000
0x00000004
0x00000008
0x0000000C
0x0000002C
0x00000038
0x00000040
0x0000003C
Initial MSP value
Reset vector
NMI vector
Hard fault vector
Reserved
PendSV
SysTick
External Interrupts
Reserved
SVCall
0x00000010
0x00000030
Address

## Slide 11: Cortex-M4 Program Image
Vector table
  Contains the starting addresses of exceptions (vectors) and the value of the main stack point (MSP)
  Can be programed in either C or assembly
C Start-up code
  Used to set up data memory and the initialization values for global data variables
  Is inserted by compiler/ linker automatically, labelled as “__main” by ARM compiler, or “_start” by GNU C compiler

## Slide 12: Cortex-M4 Program Image
Program code
  Program code refers the instructions generated from your application program. The type of data in the program code includes:
    Initial values of variables – the local variables that initialized in functions or subroutines during program execution time
    Constants – used in data values, address of peripherals, character strings, etc…
      Sometimes are stored together in data blocks called literal pools
      Additionally, constant data such as lookup tables, graphics image data (e.g. bit map) can also be merged into the program images
C library code
  Object codes that inserted to the program image by the linkers

## Slide 13: Program Image in Global Memory
The program image is stored in the code region in the global memory
  Up to 512 MB memory space range from 0x00000000 to 0x1FFFFFFF
  Usually implemented on non-volatile memory, such as on-chip FLASH memory
  Normally separated from program data, which is allocated in the SRAM region (or data region)
External RAM
Peripherals
SRAM Region
Code Region
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
Mainly used for data memory
e.g. on-chip SRAM, SDRAM
Mainly used for program image
e.g. on-chip FLASH
Global memory space

## Slide 14: Program Data

## Slide 15: How is Data Stored in RAM
Typically, the data can be divided in three sections: static data, stack, and heap:
  Static data – contains global variables and static variables
  Stack – contains the temporary data for local variables, parameter passing in function calls, registers saving during exceptions, etc.
  Heap – contains the pieces of memory spaces that dynamically reserved by function calls, such as “alloc()”, “malloc()”
Memory
Address
Grow
Downwards
High
Stack
Static
Data
Heap
Grow
Upwards
Low

## Slide 16: Define Stack and Heap
The stack and heap can be defined in either C language (with linker file) or assembly language, for example in C:
/* Set stack and heap parameters */
#define STACK_BASE 0x10020000 // stack start address
#define STACK_SIZE 0x5000 // length of the stack
#define HEAP_BASE 0x10001000 // heap starts address
#define HEAP_SIZE 0x10000 – 0x6000 // heap length
/* inker generated stack base addresses */
extern unsigned int Image$$ARM_LIB_STACK$$ZI$$Limit
extern unsigned int Image$$ARM_LIB_STACKHEAP$$ZI$$Limit
…

## Slide 17: Define Stack and Heap
Define stack and heap in assembly language:
Stack_Size EQU 0x00000400 ; 256KB of STACK
AREA STACK, NOINIT, READWRITE, ALIGN=4
Stack_Mem SPACE Stack_Size
__initial_sp
Heap_Size EQU 0x00000400 ; 1MB of HEAP
AREA HEAP, NOINIT, READWRITE, ALIGN=4
__heap_base
Heap_Mem SPACE Heap_Size
__heap_limit

## Slide 18: Data Types
A number of standard data types are supported by the C language
However, their implementation is depending on the processor architecture and C compiler
In ARM programming, the data size is referred as byte, half word, word, and double word:
  Byte: 8-bit;
  Half word: 16-bit;
  Word: 32-bit
  Double word: 64-bit
The following table shows the implementation of different data types

## Slide 19: Data Types
Data type | Size | Signed range | Unsigned range
char, int8_t, uint8_t | Byte | -128 to 127 | 0 to 255
short, int16_t, uint16_t | Half word | -32768 to 32767 | 0 to 65535
int, int32_t, uint32_t, long | Word | -2147483648 to 2147483647 | 0 to 4294967295
long long, int64_t, uint64_t | Double word | -263 to 263-1 | 0 to 264-1
float | Word | -3.4028234 × 1038 to 3.4028234 × 1038 | 
double, long double | Double word | -1.7976931348623157 ×10308 to 1.7976931348623157 ×10308 | 
pointers | Word | 0x00 to 0xFFFFFFFF | 
enum | Byte/ half word/ word | Smallest possible data type | 
bool (C++), _bool(C) | Byte | True or false | 
wchar_t | Half word | 0 to 65535 | 

## Slide 20: Data Types and Class Qualifiers
Const
  Never written by program, can be put in ROM to save RAM
Volatile
  Can be changed outside of normal program flow: ISR, hardware register
  Compiler must be careful with optimizations
Static
  Declared within function, retains value between function invocations
  Scope is limited to function

## Slide 21: Example of Data Storage
Heap data
Initialized static data
Stack data
Zero-Initialized static data
Usually stored in volatile memories, e.g. SRAM
Usually stored in non-volatile memories, e.g. FLASH
Runtime Library Code
Initialization Data
Constant data
Program code
.text
Startup Code
int a, b;
const char c=123;
int d=31;
void main(void) {
int i;
char f[32];
int *array;
array =(int*)malloc(128);
e = d + 7;
printf(“Hello!”);
}

## Slide 22: Define Interrupt Vector in C
The interrupt vector can be defined in either C language or assembly language, for example in C:
typedef void(* const ExecFuncPtr)(void) __irq;
#pragma arm section rodata="exceptions_area”
ExecFuncPtr exception_table[] = {
(ExecFuncPtr)&Image$$ARM_LIB_STACK$$ZI$$Limit, /* Initial SP */
(ExecFuncPtr)__main, /* Initial PC */
NMIException,
HardFaultException,
MemManageException,
BusFaultException,
UsageFaultException,
0, 0, 0, 0, /* Reserved */
SVCHandler,
DebugMonitor,
0, /* Reserved */
PendSVC,
SysTickHandler
/* Configurable interrupts start here...*/
};
#pragma arm section

## Slide 23: Accessing Peripherals in C
Define base addresses for peripherals, e.g.
Write a value to a peripheral register, e.g.
Read a value from a peripheral register, e.g.
#define FLASH_BASE *((volatile unsigned long *) (0x00000000UL)
#define RAM_BASE *((volatile unsigned long *) (0x10000000UL)
#define GPIO_BASE *((volatile unsigned long *) (0x2009C000UL)
#define APB0_BASE *((volatile unsigned long *) (0x40000000UL)
#define AHB_BASE *((volatile unsigned long *) (0x50000000UL)
#define CM3_BASE *((volatile unsigned long *) (0xE0000000UL)
//store a value to the memory
RAM_BASE = 0x3FFFF
//read a value from the memory
i= RAM_BASE;

## Slide 24: Use Bit-band Operation in Assembly
For example, in order to set bit[3] in word data in address 0x20000000:
  Read-Modify-Write operation
    Read the real data address (0x20000000)
    Modify the desired bit (retain other bits unchanged)
    Write the modified data back
  Bit-band operation
    Directly set the bit by writing ‘1’ to address 0x2200000C, which is the alias address of forth bit of the 32-bit data at 0x20000000
;Read-Modify-Write Operation
LDR R1, =0x20000000 ;Setup address
LDR R0, [R1] ;Read
ORR.W R0, #0x8 ;Modify bit
STR R0, [R1] ;Write back
;Bit-band Operation
LDR R1, =0x2200000C ;Setup address
MOV R0, #1 ;Load data
STR R0, [R1] ;Write

## Slide 25: Use Bit-band Operation in C
The bit-band operation is not natively supported in most C compilers
To make ease use of the bit-band feature, the address and the bit-band address can be separately declared, for example:
Alternatively, use C macros to easily access bit-band alias, for example:
#define RAM_Data1 *((volatile unsigned long *)(0x20000000))
#define RAM_Data1_Bit0 *((volatile unsigned long *)(0x22000000))
#define RAM_Data1_Bit1 *((volatile unsigned long *)(0x22000004))
RAM_Data1= RAM_Data1 | 0x01 ;Setup bit0 without using bitband
RAM_Data1_Bit0= 0x00 ;clear bit0 using bitband
RAM_Data1_Bit1= 0x01 ;Setup bit1 using bitband
#define RAM_Data1 *((volatile unsigned long *)(0x20000000))
#define BitBand(data_addr, bit) ((data_addr & 0x0F0000000) + 0x2000000 +
((data_addr & 0xFFFFF)<<5)+(bit<<2))
#define Data_Addr (data_addr) *((volatile unsigned long*)(data_addr))
Data_Addr(BitBand(RAM_Data1,0)) = 0x01 ;set bit0

## Slide 26: Mixed Assembly and C Programming

## Slide 27: Calling a C Function from Assembly
When a C function is called from an assembly file, the following areas should be aware:
  Register R0, R1, R2, R3, R12, and LR could be changed, hence it is better to save them to the stack
  The value of SP should be aligned to a double-word address boundary
  Input parameters have to be stored in the correct registers, for example, registers R0 to R3 can be used for passing four parameters
  The return value is usually stored in R0

## Slide 28: Calling a C Function from Assembly
For example, write an adding function in C:
Call the C function from the assembly code, for example:
int my_add(int x1, int x2, int x3, int x4) {
return (x1+x2+x3+x4);
}
MOVS R0, #0X1 ; parameter x1
MOVS R1, #0X3 ; parameter x2
MOVS R2, #0X5 ; parameter x3
MOVS R3, #0X7 ; parameter x4
IMPORT my_add
BL my_add ; call “my_add” function in C

## Slide 29: Calling an Assembly Function from C
When calling an assembly function from C code, following areas should be aware:
  If registers R4 to R11 need to be changed, they have to be stacked and restored in the assembly function
  If another function is called inside the assembly function, LR register needs to be saved on the stack and used for return
  The function return value is normally stored in R0

## Slide 30: Calling an Assembly Function from C
Write a function in assembly, for example:
Calling an assembly function in C, for example:
EXPORT add_asm
add_asm FUNCTION
ADDS R0, R0, R1
ADDS R0, R0, R2
ADDS R0, R0, R3
BX LR ; result is returned in R0
ENDFUNC
external int add_asm( int k1, int k2, int k3, int k4);
void main {
int x;
x = add_asm (11,22,33,44); // call assembly function
…
}

## Slide 31: Embedded Assembly
The embedded assembler allows developer to write assembly functions inside C files, for example in C:
_asm int add_asm( int k1, int k2, int k3, int k4) {
ADDS R0, R0, R1
ADDS R0, R0, R2
ADDS R0, R0, R3
BX LR
}
void main {
int x;
x = add_asm (11,22,33,44); // call assembly function
…
}

## Slide 32: Lab Exercise
Lab Exercises
  Lab 1 - processing text in assembly language
    Execute assembly code on the mbed board (e.g. Nucleo F401RE) using the debugger (in ARM® Keil® MDK )
    Examine its execution at the processor level
  Lab 2 - square root approximation
    Write an assembly code subroutine to approximate the square root of an argument using the bisection method
    Test your result on the mbed board (e.g. Nucleo F401RE) using the debugger (Keil MDK)
Nucleo F401RE

## Slide 33: ARM Keil® MDK
Keil μVision has an Integrated Development Environment (IDE), which allows user to build a project easily and quickly, the IDE includes:
  Project management;
  Make facilities;
  Source code editing;
  Program debugging;
  Complete simulation;
A serial of ARM-based tools are
integrated in Keil μVision, including:
  Compiler
  Assembler
  Linker
  Format Converter
  Libraries

## Slide 34: Useful Resources
Cortex-M4 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0439d/DDI0439D_cortex_m4_processor_r0p1_trm.pdf
Cortex-M4 Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0553a/DUI0553A_cortex_m4_dgug.pdf
STM32 Nucleo Reference Manual:
  http://www.st.com/web/en/resource/technical/document/reference_manual/DM00096844.pdf
“The Definitive Guide to ARM Cortex-M3 and Cortex-M4 Processors” by Joseph Yiu, ISBN 13: 9780124080829 ISBN 10: 0124080820, 13 December 2013