## Slide 1: Digital Input and Output

## Slide 2: Module Syllabus
Digital Input and Output
  Voltages and Logic Values
GPIO Controller
  Using Pointer to Access GPIO
  Define Data Structure for Peripherals
Digital IO Examples
  Using LED
  Using 7-Segment Display
  Using Infrared Emitter/ Detector

## Slide 3: Basic Programming – Digital IO

## Slide 4: Voltages and Logic Values
In digital devices, logic values (‘1’ or ‘0’) are represented as electrical voltages
Different devices may use different voltages to represent a logic value
  For example, the external pins of Nucleo F401RE platform use 3.3 volts for logic ‘1’, and 0 volts for logic ‘0’
Digital logic can however have different meanings in different contexts depending on the interpretation we give to different voltage levels
Logic | Voltage | Boolean | Circuit | Switch
‘1’ | 3.3V | True | Closed | On
‘0’ | 0V | False | Open | Off

## Slide 5: GPIO Design
Normally, the external pins are not directly accessible, but accessed via a peripheral called General-purpose input/output (GPIO)
  Used for general purpose, no special usage defined
  Widely used for most applications
  The direction of input/ output is controlled by the direction register
  A mask register is often used to mask out certain bits
Pin
Function Select
…
Memory Mapped I/O
Alternate Function 1
Alternate Function 2
Alternate Function n

## Slide 6: GPIO Design
GPIO pins split into groups, called ports
  Each port has 32 pins [31:0]
  Each of the ports are connected to the microcontroller via the peripheral bridge
To reduce power consumption clocks are turned off for particular areas
  Default setting – clock is disabled
  To use a peripheral or a resource clock has to be enabled for each item individually
Each pin is connected to a multiplexer
  Allows each pin to perform several functions
  Optimizes functionality small packages
  Signal multiplexer and other pin options can be configured in the Pin Control Register (PCR)

## Slide 7: GPIO Registers
For example, in the Nucleo F401RE MCU, there are eight GPIO peripherals named from PORTA-PORTH, and each of them has 10 registers, which include:
  Port Mode Register (MODER) - configure the I/O direction mode (input/output/alternate/analog)
  Output Type Register (TYPER) – configure the output type of the I/O port (push-pull/open-drain)
  Output Speed Register (OSPEEDR) – configure the I/O output speed (2/25/50/100 MHz)
  Pull-Up/Pull-Down Register (PUPDR) – configure the I/O pull-up or pull-down (no pull-up, pull-down/pull-up/pull-down)
  Input Data Register (IDR) – contain the input value of the corresponding I/O port
  Output Data Register (ODR) – can be read and written by software (ODR bits can be individually set and reset by writing to the BSRR)
  Bit Set/Reset Register (BSRR) – can be used for atomic bit set/reset
  Configuration Lock Register (LCKR) – used to lock the configuration of the port bits when a correct write sequence is applied to bit 16
  Alternate Function Low Register (AFRL) – configure alternate function I/Os
  Alternate Function High Register (AFRH) – configure alternate function I/Os

## Slide 8: Using Pointer to Access GPIO
Normally, you can use a pointer to directly access a GPIO peripheral in either C or assembly. For example in C, to light an LED on PB_10:
This solution is fine for simple applications. However, if multiple instantiations of the same type of peripheral are available at the same time, we will need to define registers for each peripheral, which makes code maintenance difficult
On the other hand, since each register is defined as a separate pointer, each register access requires a 32-bit address constant. As a result, the program image will consume a larger memory space.
#define RCC_AHB1ENR (*((volatile unsigned long *) 0x40023830))
#define GPIOB_MODER (*((volatile unsigned long *) 0x40020400))
#define GPIOB_PUPDR (*((volatile unsigned long *) 0x40020408))
#define GPIOB_OSPEEDR (*((volatile unsigned long *) 0x4002040C))
#define GPIOB_ODR (*((volatile unsigned long *) 0x40020414))
RCC_AHB1ENR |= 0x02;
GPIOB_MODER |= 0x00100000;
GPIOB_PUPDR |= 0x00200000;
GPIOB_OSPEEDR |= 0x00200000;
GPIOB_ODR |= 0x0400;

## Slide 9: Define Data Structure for Peripherals
To further simplify the code and reduce its length, we can:
  Define the peripheral register set as a data structure,
  Define the peripheral as a memory pointer to this data structure:
For example:
typedef struct {
volatile unsigned int MODER;
volatile unsigned int OTYPER;
volatile unsigned int OSPEEDR;
volatile unsigned int PUPDR;
volatile unsigned int IDR;
volatile unsigned int ODR;
volatile unsigned int BSRRL;
volatile unsigned int BSRRH;
volatile unsigned int LCKR;
volatile unsigned int AFR[2];
} GPIO_TypeDef;

## Slide 10: Define Data Structure for Peripherals
Then, to turn on an LED on PB_10:
#define GPIOB_BASE 0x40020400
#define GPIOB ((GPIO_TypeDef *) GPIOB_BASE )
RCC -> AHB1ENR |= 0x02;
GPIOB -> MODER |= 0x00100000;
GPIOB -> PUPDR |= 0x00200000;
GPIOB -> OSPEED |= 0x00200000;
GPIOB -> ODR |= 0x0400;

## Slide 11: Define Data Structure for Peripherals
With such arrangement:
  The same register data structure for the peripheral can be shared between multiple instantiations
  Hence code maintenance is easier
  The requirement for immediate data storage is reduced
  Compiled code is smaller, giving better code density
With further modification, the functions developed for one peripheral can be shared between multiple instantiations by passing the base pointer to the function, for example:
#define GPIOA ((GPIO_TypeDef *) GPIOA_BASE )
#define GPIOB ((GPIO_TypeDef *) GPIOB_BASE )
#define GPIOC ((GPIO_TypeDef *) GPIOC_BASE )
void GPIO_init (GPIO_TypeDef *GPIO_pointer) {
GPIOB -> MODER |= 0x00100000;
GPIOA -> MODER |= 0x00010000;
}

## Slide 12: Digital IO Example: LEDs
Light-Emitting Diode (LED)
  Emits light when switched on
  Simplest way to indicate the status of logic
  Also widely used in applications such as automotive lighting, general lighting, traffic signals etc.
Vcc 3.3V
Digital Output
Digital Output
GND
LED
ID
ID
R
R
LED
Digital output sources current to LED
Digital output sinks current from LED

## Slide 13: Digital IO Example: 7-Segment Display
Use 7 segments and a dot to display numerals or letters
Widely used in digital electronic devices, such as digital clocks, electronic meters
Simple control, easy to debug
Different values can be represented by different combinations of 8-bit segments (including dot), for example:
Display | 0 | 1 | 2 | 3 | 4
8-bit value | 00111111 | 00000110 | 01011011 | 01001111 | 01100110
Display | 5 | 6 | 7 | 8 | 9
8-bit value | 01101101 | 01111101 | 00000111 | 01111111 | 01101111

## Slide 14: Digital IO Example: Infrared Emitter/Detector
Infrared emitter (LED)
  A light-emitting diode that emits invisible infrared (IR) when conducting e.g. when connected to digital output:
    ‘1’ – IR emitted (or brightness above a threshold)
    ‘0’ – no IR emitted (or brightness below a threshold)
Infrared detector (photodiode)
  Converts light into either current or voltage e.g. when connected to digital input:
    ‘1’ – IR received (or brightness above a threshold)
    ‘0’ – no IR received (or brightness below a threshold)
Vcc 3.3V
Digital Input
Digital Output
GND
Infrared emitter
R
R
Infrared detector

## Slide 15: Useful Resources
Cortex-M4 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0439d/DDI0439D_cortex_m4_processor_r0p1_trm.pdf
Cortex-M4 Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0553a/DUI0553A_cortex_m4_dgug.pdf
STM32 Nucleo Reference Manual:
  http://www.st.com/web/en/resource/technical/document/reference_manual/DM00096844.pdf