## Slide 1: Interrupts and Low Power Features

## Slide 2: Module Syllabus
Interrupts
  What are interrupts?
  Why use interrupts?
Interrupts
  Entering an Exception Handler
  Exiting an Exception Handler
Port Module and External Interrupts
Timing Analysis
Program Design with Interrupts

## Slide 3: Example System with Interrupt
Goal: change the colour of the RGB LED when switch is pressed
Need to add an external switch
  (resistor is internal – a pull-up resistor)

## Slide 4: How to Detect when a Switch is Pressed?
Polling – use software to regularly check it
  Slow – need to explicitly check to see if switch is pressed
  Wasteful of CPU time – the faster a response we need, the more often we need to check
  Scales badly – difficult to build a system with many activities which can respond quickly. Response time depends on all other processing.
Interrupt – use special hardware in MCU to detect event and run ISR in response
  Efficient – code runs only when necessary
  Fast – hardware mechanism
  Scales well
          ISR response time doesn’t depend on most other processing
          Code modules can be developed independently

## Slide 5: Interrupt or Exception Processing Sequence
Main code is running
Interrupt trigger occurs
  Processor does some hard-wired processing
  Processor executes the ISR, including return-from-interrupt instruction at the end
Processor resumes to main code
Main Code
Hardwired CPU response activities
Interrupt Routine
Time

## Slide 6: Interrupts
Hardware-triggered asynchronous software routine
  Triggered by hardware signal from peripheral or external device
  Asynchronous – can happen anywhere in the program (unless interrupt is disabled)
  Software routine – Interrupt Service Routine runs in response to interrupt
Fundamental mechanism of microcontrollers
  Provides efficient event-based processing rather than polling
  Provides quick response to events regardless of program state, complexity, location
  Allows many multithreaded embedded systems to be responsive without an operating system (specifically task scheduler)

## Slide 7: Example Program Requirements & Design
When switch SW is pressed, ISR will increment count variable
Main code will light LEDs according to count value in binary sequence (Blue: 4, Green: 2, Red: 1)
Main code will toggle its debug line each time it executes
ISR will raise its debug line (and lower main’s debug line) whenever it is executing
SW
ISR
count
MAIN
RGB LED
Global Variable
MAIN
ISR
(does initialization, then updates LED based on count)

## Slide 8: Example Exception Handler
We will examine processor’s response to exception in detail

## Slide 9: Use Debugger for Detailed Processor View
Can see registers, stack, source code, disassembly (object code)
Note: Compiler may generate code for function entry
Place breakpoint on Handler function declaration line in source code, not at first line of code

## Slide 10: Entering an Exception Handler

## Slide 11: CPU’s Hardwired Exception Processing
Finish current instruction
  Except for lengthy instructions
Push context (registers) onto current stack (MSP or PSP)
  xPSR, Return Address, LR(R14), R12, R3, R2, R1, R0
Switch to handler/privileged mode, use MSP
Load PC with address of interrupt handler
Load LR with EXC_RETURN code
Load IPSR with exception number
Start executing code of interrupt handler
Usually 16 cycles from exception request to execution of first instruction in handler

## Slide 12: 1. Finish Current Instruction
Most instructions are short and finish quickly
Some instructions may take many cycles to execute
  Load Multiple (LDM), Store Multiple (STM), Push, Pop, MULS (32 cycles for some CPU core implementations)
This will delay interrupt response significantly
If one of these is executing when the interrupt is requested, the processor:
  abandons the instruction
  responds to the interrupt
  executes the ISR
  returns from interrupt
  restarts the abandoned instruction

## Slide 13: 2. Push Context onto Current Stack
Two SPs: Main (MSP), process (PSP)
Which is active depends on operating mode, CONTROL register bit 1
Stack grows toward smaller addresses
 |  | <previous> | SP points here before interrupt
 | SP + 0x1C | xPSR | 
 | SP + 0x18 | PC | 
Decreasing | SP + 0x14 | LR | 
memory | SP + 0x10 | R12 | 
address | SP + 0x0C | R3 | 
 | SP + 0x08 | R2 | 
 | SP + 0x04 | R1 | 
 | SP + 0x00 | R0 | SP points here upon entering ISR

## Slide 14: Context Saved on Stack
Saved R0
Saved R1
Saved R2
Saved R3
Saved R12
Saved LR
Saved PC
Saved xPSR
SP value is reduced since registers have been pushed onto stack

## Slide 15: 3. Switch to Handler/Privileged Mode
Handler mode always uses Main SP
Thread
Mode. MSP or PSP.
Handler Mode
MSP
Reset
Starting Exception Processing
Exception Processing
Completed

## Slide 16: Handler and Privileged Mode
Mode changed to Handler. Was already using MSP

## Slide 17: Update IPSR with Exception Number
Exception number 0x10 (interrupt number + 0x10)

## Slide 18: 4. Load PC With Address Of Exception Handler
The program counter is selected from the vector table depending on exception
Memory Address | Value
0x0000_0000 | Initial Stack Pointer
0x0000_0004 | Reset
0x0000_0008 | NMI_IRQHandler
… | 
 | IRQ0_Handler
 | IRQ1_Handler
… | 
Reset: | 
… | 
NMI_IRQHandler: | 
… | 
IRQ0_Handler: | 
… | 
IRQ1_Handler: | 

## Slide 19: Can Examine Vector Table With Debugger
Why is the vector odd?
LSB of address indicates that handler uses Thumb code
Exception number | IRQ number | Vector | Offset
 |  | Initial SP | 0x00
1 |  | Reset | 0x04
2 | -14 | NMI | 0x08
3 | -13 | HardFault | 0x0C
4 |  | Reserved | 0x10
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
11 | -5 | SVCall | 0x2C
12 |  | Reserved | 
13 |  |  | 
14 | -2 | PendSV | 0x38
15 | -1 | SysTick | 0x3C
16 | 0 | IRQ0 | 0x40
17 | 1 | IRQ1 | 0x44
18 | 2 | IRQ2 | 0x48
. |  | . | 
16+n | n | IRQn | 0x40+4n

## Slide 20: Upon Entry to Handler
PC has been loaded with start address of handler

## Slide 21: 5. Load LR With EXC_RETURN Code
EXC_RETURN value generated by CPU to provide information on how to return
  Which SP to restore registers from? MSP (0) or PSP (1)
          Previous value of SPSEL
  Which mode to return to? Handler (0) or Thread (1)
          Another exception handler may have been running when this exception was requested
EXC_RETURN | Return Mode | Return Stack | Description
0xFFFF_FFF1 | 0 (Handler) | 0 (MSP) | Return to exception handler
0xFFFF_FFF9 | 1 (Thread) | 0 (MSP) | Return to thread with MSP
0xFFFF_FFFD | 1 (Thread) | 1 (PSP) | Return to thread with PSP

## Slide 22: Updated LR With EXC_RETURN Code

## Slide 23: 6. Start Executing Exception Handler
Exception handler starts running, unless preempted by a higher-priority exception
Exception handler may save additional registers on stack
  E.g. if handler may call a subroutine, LR and R4 must be saved

## Slide 24: After Handler Has Saved More Context
Saved R4
Saved LR
Saved R0
Saved LR
Saved PC
Saved xPSR
Saved R3
Saved R12
Saved R1
Saved R2
SP value reduced since registers have been pushed onto stack

## Slide 25: Exiting an Exception Handler

## Slide 26: Exiting an Exception Handler
Execute instruction triggering exception return processing
Select return stack, restore context from that stack
Resume execution of code at restored address

## Slide 27: 1. Execute Instruction for Exception Return
No “return from interrupt” instruction
Use regular instruction instead
  BX LR - Branch to address in LR by loading PC with LR contents
  POP …, PC - Pop address from stack into PC
… with a special value EXC_RETURN loaded into the PC to trigger exception handling processing
  BX LR used if EXC_RETURN is still in LR
  If EXC_RETURN has been saved on stack, then use POP

## Slide 28: What Will Be Popped from Stack?
R4: 0x4040_0000
PC: 0xFFFF_FFF9
Saved R4
Saved LR
Saved R0
Saved LR
Saved PC
Saved xPSR
Saved R3
Saved R12
Saved R1
Saved R2

## Slide 29: 2. Select Stack, Restore Context
Check EXC_RETURN (bit 2) to determine from which SP to pop the context
Pop the registers from that stack
EXC_RETURN | Return Stack | Description
0xFFFF_FFF1 | 0 (MSP) | Return to exception handler with MSP
0xFFFF_FFF9 | 0 (MSP) | Return to thread with MSP
0xFFFF_FFFD | 1 (PSP) | Return to thread with PSP
 |  | <previous> | SP points here after handler
 | SP + 0x1C | xPSR | 
 | SP + 0x18 | PC | 
Decreasing | SP + 0x14 | LR | 
memory | SP + 0x10 | R12 | 
address | SP + 0x0C | R3 | 
 | SP + 0x08 | R2 | 
 | SP + 0x04 | R1 | 
 | SP + 0x00 | R0 | SP points here during handler

## Slide 30: Example
PC=0xFFFF_FFF9, so return to thread mode with main stack pointer
Pop exception stack frame from stack back into registers
Saved R0
Saved R1
Saved R2
Saved R3
Saved R12
Saved LR
Saved PC
Saved xPSR

## Slide 31: Resume Executing Previous Main Thread Code
Exception handling registers have been restored: R0, R1, R2, R3, R12, LR, PC, xPSR
SP is back to previous value
Back in thread mode
Next instruction to execute is at 0x0000_0A70

## Slide 32: Processor Core Interrupts

## Slide 33: Microcontroller Interrupts
Types of interrupts
  Hardware interrupts
          Asynchronous: not related to what code the processor is currently executing
          Examples: interrupt is asserted, character is received on serial port, or ADC converter finishes conversion
  Exceptions, Faults, software interrupts
          Synchronous: are the result of specific instructions executing
          Examples: undefined instructions, overflow occurs for a given instruction
  We can enable and disable (mask) most interrupts as needed (maskable), others are non-maskable
Interrupt service routine (ISR)
  Subroutine which processor is forced to execute to respond to a specific event
  After ISR completes, MCU goes back to previously executing code

## Slide 34: Nested Vectored Interrupt Controller
NVIC manages and prioritizes external interrupts
Interrupts are types of exceptions
  Exceptions 16 through 16+N
Modes
  Thread Mode: entered on Reset
  Handler Mode: entered on executing an exception
Privilege level
Stack pointers
  Main Stack Pointer, MSP
  Process Stack Pointer, PSP
Exception states: Inactive, Pending, Active, A&P
ARM Cortex Core
Port Module
NVIC
Next Module
Another Module

## Slide 35: NVIC Registers and State
Enable - Allows interrupt to be recognized
  Accessed through two registers (set bits for interrupts)
          Set enable with NVIC_ISER, clear enable with NVIC_ICER
  CMSIS Interface: NVIC_EnableIRQ(IRQnum), NVIC_DisableIRQ(IRQnum)
Pending - Interrupt has been requested but is not yet serviced
  CMSIS: NVIC_SetPendingIRQ(IRQnum), NVIC_ClearPendingIRQ(IRQnum)

## Slide 36: Core Exception Mask Register
Similar to “Global interrupt disable” bit in other MCUs
PRIMASK - Exception mask register (CPU core)
  Bit 0: PM Flag
          Set to 1 to prevent activation of all exceptions with configurable priority
          Clear to 0 to allow activation of all exception
  Access using CPS, MSR and MRS instructions
  Use to prevent data race conditions with code needing atomicity
CMSIS-CORE API
  void __enable_irq() - clears PM flag
  void __disable_irq() - sets PM flag
  uint32_t __get_PRIMASK() - returns value of PRIMASK
  void __set_PRIMASK(uint32_t x) - sets PRIMASK to x

## Slide 37: Prioritization
Exceptions are prioritized to order the response simultaneous requests (smaller number = higher priority)
Priorities of some exceptions are fixed
  Reset: -3, highest priority
  NMI: -2
  Hard Fault: -1
Priorities of other (peripheral) exceptions are adjustable
  Value is stored in the interrupt priority register (IPR0-7)
  0x00
  0x40
  0x80
  0xC0

## Slide 38: Special Cases of Prioritization
Simultaneous exception requests?
  Lowest exception type number is serviced first
New exception requested while a handler is executing?
  New priority higher than current priority?
          New exception handler preempts current exception handler
  New priority lower than or equal to current priority?
          New exception held in pending state
          Current handler continues and completes execution
          Previous priority level restored
          New exception handled if priority level allows

## Slide 39: Timing Analysis

## Slide 40: Big Picture Timing Behavior
Switch was pressed for about 0.21 s
ISR runs in response to switch signal’s falling edge
Main seems to be running continuously (signal toggles between 1 and 0)
  Does it really? You will investigate this in the lab exercise.

## Slide 41: Interrupt Response Latency
Latency = time delay
Why do we care?
  This is overhead which wastes time, and increases as the interrupt rate rises
  This delays our response to external events, which may or may not be acceptable for the application, such as sampling an analog waveform
How long does it take?
  Finish executing the current instruction or abandon it
  Push various registers on to the stack, fetch vector
          CIntResponseOvhd: Overhead for responding to each interrupt
  If we have external memory with wait states, this takes longer

## Slide 42: Maximum Interrupt Rate
We can only handle so many interrupts per second
  FMax_Int: maximum interrupt frequency
  FCPU: CPU clock frequency
  CISR: Number of cycles ISR takes to execute
  COverhead: Number of cycles of overhead for saving state, vectoring, restoring state, etc.
  FMax_Int = FCPU/(CISR+ COverhead)
  Note that model applies only when there is one interrupt in the system
When processor is responding to interrupts, it isn’t executing our other code
  UInt: Utilization (fraction of processor time) consumed by interrupt processing
  UInt = 100%*FInt* (CISR+COverhead)/ FCPU
  CPU looks like it’s running the other code with CPU clock speed of (1-UInt)*FCPU

## Slide 43: Program Design with INterrupts

## Slide 44: Program Design with Interrupts
How much work to do in ISR?
Should ISRs re-enable interrupts?
How to communicate between ISR and other threads?
  Data buffering
  Data integrity and race conditions

## Slide 45: How Much Work Is Done in ISR?
Trade-off: Faster response for ISR code will delay completion of other code
In system with multiple ISRs with short deadlines, perform critical work in ISR and buffer partial results for later processing

## Slide 46: Sharing Data Safely between ISRs and other Threads

## Slide 47: Overview
Volatile data – can be updated outside of the program’s immediate control
Non-atomic shared data – can be interrupted partway through read or write, is vulnerable to race conditions

## Slide 48: Volatile Data
Compilers assume that variables in memory do not change spontaneously, and optimize based on that belief
  Don’t reload a variable from memory if current function hasn’t changed it
  Read variable from memory into register (faster access)
  Write back to memory at end of the procedure, or before a procedure call, or when compiler runs out of free registers
This optimization can fail
  Example: reading from input port, polling for key press
          while (SW_0) ; will read from SW_0 once and reuse that value
          Will generate an infinite loop triggered by SW_0 being true
Variables for which it fails
  Memory-mapped peripheral register – register changes on its own
  Global variables modified by an ISR – ISR changes the variable
  Global variables in a multithreaded application – another thread or ISR changes the variable

## Slide 49: The Volatile Directive
Need to tell compiler which variables may change outside of its control
  Use volatile keyword to force compiler to reload these vars from memory for each use volatile unsigned int num_ints;
  Pointer to a volatile int volatile int * var; // or int volatile * var;
  Now each C source read of a variable (e.g. status register) will result in an assembly language LDR instruction
  Good explanation in Nigel Jones’ “Volatile,” Embedded Systems Programming July 2001

## Slide 50: Non-Atomic Shared Data
Want to keep track of current time and date
Use 1 Hz interrupt from timer
System
  current_time structure tracks time and days since some reference event
  current_time’s fields are updated by periodic 1 Hz timer ISR
void GetDateTime(DateTimeType * DT){
DT->day = current_time.day;
DT->hour = current_time.hour;
DT->minute = current_time.minute;
DT->second = current_time.second;
}
void DateTimeISR(void){
current_time.second++;
if (current_time.second > 59){
current_time.second = 0;
current_time.minute++;
if (current_time.minute > 59) {
current_time.minute = 0;
current_time.hour++;
if (current_time.hour > 23) {
current_time.hour = 0;
current_time.day++;
… etc.
}

## Slide 51: Example: Checking the Time
Problem
  An interrupt at the wrong time will lead to half-updated data in DT
Failure Case
  current_time is {10, 23, 59, 59} (10th day, 23:59:59)
  Task code calls GetDateTime(), which starts copying the current_time fields to DT: day = 10, hour = 23
  A timer interrupt occurs, which updates current_time to {11, 0, 0, 0}
  GetDateTime() resumes executing, copying the remaining current_time fields to DT: minute = 0, second = 0
  DT now has a time stamp of {10, 23, 0, 0}.
  The system thinks time just jumped backwards one hour!
Fundamental problem – “race condition”
  Preemption enables ISR to interrupt other code and possibly overwrite data
  Must ensure atomic (indivisible) access to the object
          Native atomic object size depends on processor’s instruction set and word size.
          Is 32 bits for ARM

## Slide 52: Examining the Problem More Closely
Must protect any data object which both:
  Requires multiple instructions to read or write (non-atomic access), and
  Is potentially written by an ISR
How many tasks/ISRs can write to the data object?
  One? Then we have one-way communication
          Must ensure the data isn’t overwritten partway through being read
              Writer and reader don’t interrupt each other
  More than one?
          Must ensure the data isn’t overwritten partway through being read
            Writer and reader don’t interrupt each other
          Must ensure the data isn’t overwritten partway through being written
            Writers don’t interrupt each other

## Slide 53: Definitions
Race condition: Anomalous behavior due to unexpected critical dependence on the relative timing of events. Result of example code depends on the relative timing of the read and write operations.
Critical section: A section of code which creates a possible race condition. The code section can only be executed by one process at a time. Some synchronization mechanism is required at the entry and exit of the critical section to ensure exclusive use.

## Slide 54: Solution: Briefly Disable Preemption
Prevent preemption within critical section
If an ISR can write to the shared data object, need to disable interrupts
  save current interrupt masking state in m
  disable interrupts
Restore previous state afterwards (interrupts may have already been disabled for another reason)
Use CMSIS-CORE to save, control and restore interrupt masking state
Avoid if possible
  Disabling interrupts delays response to all other processing requests
  Make this time as short as possible (e.g. a few instructions)
void GetDateTime(DateTimeType * DT){
uint32_t m;
m = __get_PRIMASK();
__disable_irq();
DT->day = current_time.day;
DT->hour = current_time.hour;
DT->minute = current_time.minute;
DT->second = current_time.second;
__set_PRIMASK(m);
}

## Slide 55: Useful Resources
Cortex-M4 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0439d/DDI0439D_cortex_m4_processor_r0p1_trm.pdf
Cortex-M4 Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0553a/DUI0553A_cortex_m4_dgug.pdf
Nucleo F401RE Reference Manual:
  http://www.st.com/web/en/resource/technical/document/reference_manual/DM00096844.pdf
“The Definitive Guide to ARM Cortex-M3 and Cortex-M4 Processors” by Joseph Yiu, ISBN 13: 9780124080829 ISBN 10: 0124080820, 13 December 2013